## Slide 1
An Introduction to Hardware, Software, and the Internet
Java Methods
A & AB
Object-Oriented Programming
and Data Structures
Maria Litvin ● Gary Litvin
Copyright © 2006 by Maria Litvin, Gary Litvin, and Skylight Publishing. All rights reserved.
ch 001
Notes: Two possible activities for this chapter are to look inside of an old computer and to inventory the programs installed on a new one.

## Slide 2: Objectives:
Get an overview of the main hardware components and terms: CPU, memory, peripheral devices
Learn about software: operating system and application software
Get an idea of how information is stored in computer memory
Learn basic facts about the Internet
Notes: The Internet is the best resource for more detailed information on hardware and software and the Internet itself.

## Slide 3: The text for this chapter is on the web at:
www.skylit.com/javamethods
Notes: Or go to skylit.com and click on the Java Methods Home Page link.

## Slide 4: Hardware
The CPU (Central Processing Unit) is made of millions of semiconductor devices, called transistors, etched into a silicon chip.
Transistors are combined to form logical devices called gates.
All digital electronics is basically made up of gates.
Notes: Early computers used vacuum tubes and relay switches. Semiconductor technology allows manufacturers to etch microscopic devices into layers in a silicon chip.

## Slide 5: Gates
AND gate
OR gate
NOT gate
Notes: Other types of gates work as combinations of these three: e.g., NAND is NOT and AND.

## Slide 6: Example: XOR Circuit
A AND (NOT B)
OR
(NOT A) AND B
Notes: An XOR gate (exclusive OR) has the output TRUE when one of the inputs, but not both, is TRUE.

## Slide 7: RAM, CPU, Bus
CPU
Memory (RAM)
Data bus
Address bus
Registers
Memory (ROM)
Notes: ROM is tiny as compared to RAM: ROM may be a few KB, while RAM size on personal computers and laptops is getting to be over 1 GB.
A memory address is represented as a binary number. An address is “sent” via the memory bus; the data is written or retrieved via the data bus. A “bus” is a logical device.

## Slide 8: Motherboard
CPU
RAM (SIMMs)
Extension slots
ROM
Notes: The CPU chip is packaged inside a ceramic case. The chip itself is as small as 3/4".
SIMM stands for Single Inline Memory Module.
Logically ROM and RAM form contiguous memory space; the CPU can’t just write into ROM (and never needs to try). Physically ROM is on a separate chip.
Extension slots are used for plugging in additional adapter boards: Internet adapter, graphics card, sound card, disk controller, etc. In newer systems many of these functions are built directly into the motherboard.

## Slide 9: Hardware Terms
CPU — Central Processing Unit
RAM — Random-Access Memory
  “random-access” means the CPU can read directly from and write to any memory location
  holds both data and CPU instructions
ROM — Read-Only Memory
  holds initialization and hardware diagnostic programs
Peripheral devices (secondary storage, input/output)
Notes: The idea that a computer can hold its own program in RAM is attributed to von Neumann; it was not obvious at first. The very first computers were programmed by connecting wires to sockets.
The term “peripheral devices” comes from the old era; in a laptop, most devices are integrated into one small unit. A printer or a scanner remains “peripheral.”

## Slide 10: CPU
In personal computers, the CPU is a microprocessor, contained on one chip.
The CPU speed is measured in MHz (megahertz, millions of clock cycles per second) and GHz (gigahertz, billions of cycles).
A CPU instruction takes one or several clock cycles.
Heinrich Rudolf Hertz
Notes: The first IBM PC’s CPU, Intel 8088, ran at 4.77 MHz; now the speeds are reaching 2 GHz, 500 times faster. Additional technologies, such as cashing and pipelining (fetching the next instruction while the current one is being executed) increase the speed even more. A modern microprocessor has a built-in co-processor for floating-point arithmetic.

## Slide 11: RAM
1 KB (kilobyte) = 1024 bytes
1 MB (megabyte) = 1024 · 1024 bytes
1 GB (gigabyte) = 1024 · 1024 · 1024 bytes
1 terabyte = 1024 gigabyes
0 0 1 0 1 1 0 1
bit 0
bit 7
220  106, a million
230  109, a billion
210
1 byte = 8 bits
Notes: Memory size is measured using powers of 2 because memory addresses are binary numbers. A 32-bit address bus can directly address 232 = 4 GB of memory

## Slide 12: Secondary Storage
Hard disk: 40 - 500 GB
CD-ROM: 700 MB
Optical (ZIP) disk: 100 MB - 1 GB
A file is a
software concept
Memory stick: 64 MB - 1 GB
Notes: Operating system software arranges files into a tree-like structure of folders (directories).
Data compression can further expand the storage capacity of different devices.
By comparison, the first IBM PC/XT (c. 1983) had 512 KB of RAM and a 10 MB hard disk. Thus RAM has increased 1000 times and disk space has increased 10,000 times, while the price has decreased 10 times.

## Slide 13: I/O Devices
Monitor and video adapter
Keyboard, mouse or touch pad
Sound card, speakers, microphone
Internet adapter, modem
D/A (digital-to-analog) and A/D (analog-to-digital) converters
Scanners, digital cameras, printers
Notes: A modem is used to connect to a host computer via a telephone line or cable.
The Internet adapter is used to connect to the Internet via a high-speed connection.
A/D and D/A converters are used to convert analog signals into digital and vice versa. They are used to connect analog scientific instruments or industrial controllers to a digital computer.
New types of devices and new hardware standards for connecting devices to a computer are emerging all the time. More recent computers have high-speed USB (Universal Serial Bus) ports for connecting peripherals. USB replaces old serial and other ports.

## Slide 14: Software Layers
Device drivers
Operating system
Applications
BIOS, firmware
Notes: BIOS stands for Basic Input-Output System. BIOS is in ROM; it controls the keyboard, disk drives, etc.
A device driver is a specialized program that knows how to handle a particular device or hardware adapter. For example, a printer or a scanner needs a device driver.
A few popular operating systems: Windows, Mac OS, Unix and its derivatives (e.g., Linux), OS/2, etc.
Common applications on personal computers: word processing, databases, spreadsheets, Internet browsers, music and movie players, games.

## Slide 15: Software Terms
Operating system
  a program that maintains the file system, dispatches applications, and provides other system-level services
Console application
  a program with simple text user interface
GUI — Graphical User Interface
  graphics, menus, buttons, icons, etc.
OOP — Object-Oriented Programming
Notes: More on different types of applications and OOP in Chapter 2.

## Slide 16: Software Developers Have To:
Absorb and use emerging technical information
Create sound software system architectures
Understand and devise effective algorithms
Be proficient with the syntax and style of programming languages
Diagnose and correct programming errors
Continued...
Notes: In reality, a number of people are involved in every software development project, and different people may possess different skills.

## Slide 17: Software Developers Have To:
Use software development tools and documentation
Find and utilize reusable software components
Design and implement friendly user interfaces
Uphold the highest standards of professional ethics
Notes: Sofware development entails different types of work and has room for people with different interests and skills.
The discipline that focuses on all aspects of software development is called computer science.

## Slide 18: Numbers In Memory
Integers are represented in binary (base 2)
Java uses 4 bytes for an integer (int data type)
  0 00000000
  1 00000001
  2 00000010
  3 00000011
  ... ...
  255 11111111
Notes: Java also has the long data type, which takes 8 bytes and the short data type that takes 2 bytes.

## Slide 19: Numbers In Memory (cont’d)
For signed numbers, the most significant bit indicates the sign:
Negative numbers are represented in two’s-complement form
00000000 00000000 00000000 00010001
Sign bit
1
16
17
+
11111111 11111111 11111111 11101111
Sign bit
-17
17 + (-17) = 232 = 0
Notes: 17 = 1 * 24 + 0 * 23 + 0 * 22 + 0 * 21 + 1 * 20
Negative numbers use two’s-complement representation; that is, -17 is represented as 232 - 17, and the sign bit is set to 1. So -17 + 17 gives you 0 (plus the overflow bit, which disappears).

## Slide 20: Numbers in Memory (cont’d)
Real numbers are represented as floating-point numbers (similar to scientific notation) with a sign, binary mantissa (fractional part), and binary exponent.
Java uses 8 bytes (64 bits) for a “double” (that is, double-precision) floating-point number.
double’s range is from -1.8  10308 to 1.8  10308
(but precision is only 14 significant digits)
Notes: You have to be careful when adding a very small (by absolute value) number to a very large number, because the contribution of the very small number will be lost. The range for doubles is large, but the precision is more limited.

## Slide 21: Characters
Unicode code associates characters with numbers (2 bytes represent a character).
ASCII (American Standard Code for Information Interchange) is a subset comprising the first 128 codes of Unicode:
  <space> 32  ‘A’ - ‘Z’ 65 - 90
  ‘0’ - ‘9’ 48 - 57  ‘a’ - ‘z’ 97 - 122
The first 32 codes are control codes (Carriage Return, Newline, Tab, etc.).
Notes: From the Unicode page:
“The Unicode Consortium is a non-profit organization founded to develop, extend and promote use of the Unicode Standard, which specifies the representation of text in modern software products and standards. The membership of the consortium represents a broad spectrum of corporations and organizations in the computer and information processing industry. The consortium is supported financially solely through membership dues. Membership in the Unicode Consortium is open to organizations and individuals anywhere in the world who support the Unicode Standard and wish to assist in its extension and implementation.”
Unicode represents all major alphabets of the world as well as special characters. There are provisions for ideographic characters from Japan, Korea, China, and more.

## Slide 22: The Internet
A network of interconnected computers that share common communication protocols, TCP/IP
TCP: Transmission Control Protocol
IP: Internet Protocol
Notes: A network requires network hardware (adapters, switches, etc.), communication lines (cable, phone lines, wireless, etc), and, most importantly, communication protocols, i.e., technical standards for different devices to talk to each other.

## Slide 23: The Internet Layers
Internetworking: routing and forwarding data (IP)
Transport: delivering data reliably and securely (TCP)
Applications: telnet, www, e-mail, AIM, FTP, Voice
Network technology (switches, adapters, routers)
Notes: FTP — File Transfer Protocol.
AIM — AOL Instant Messenger.
e-mail uses SMTP — Simple Mail Transfer Protocol.
www uses HTTP — HyperText Transfer Protocol.
These application-level protocols sit on top of TCP/IP.

## Slide 24: The Internet Terms
Browser
  provides convenient way to download and display information from the Internet
Search engine
  indexes and helps find the Internet documents that contain specified keywords and phrases
Portal
  a large popular web site that has a collection of links arranged by category
Notes: The two most popular browsers are Firefox and Internet Explorer, but there are many others.
Google has become the most popular search engine. Its success is due to a simple innovative idea: it ranks the “hits” (matching documents) based on how many web pages are linked to a document as opposed to how many times a search keyword appears in a document.
Yahoo is a popular general-purpose portal.

## Slide 25: The Internet Terms (cont’d)
Host
  a computer connected to a network
Server
  a computer on a network that provides a particular service (e.g., e-mail server)
URL
  Uniform (or Universal) Resource Locator, an address of a document or a resource on the Internet
Notes: With the appropriate software and an Internet connection, you can turn your computer into a host that will hold your web site. But small end-users have their web sites “hosted” by one of the commercial ISPs (Internet Service Providers). The largest is AOL.

## Slide 26: Review:
Describe the outputs of an AND gate for all possible combinations of the two inputs.
What are CPU, RAM, and ROM?
Approximately how many bytes are in a megabyte? In a gigabyte? In a terabyte?
Name six I/O devices.
Notes: Describe the outputs of an AND gate for all possible combinations of the two inputs.
  T, T ==> T
  T, F ==> F
  F, T ==> F
  F, F ==> F
What are CPU, RAM, and ROM?
Central Processing Unit (microprocessor in personal computers), Random-Access Memory (for holding data and programs), Read-Only Memory (for holding the start-up program, hardware diagnostics, and configuration program).
Approximately how many bytes are in a megabyte? In a gigabyte?
One million. One billion. One trillion.
Name six I/O devices.
Display, keyboard, mouse, sound card, printer, scanner

## Slide 27: Review (cont’d):
Is a device driver a hardware or a software entity?
Is a file a hardware or a software concept?
Describe the main difference between a console and a GUI application.
Name several skills needed for software development.
Notes: Is a device driver a hardware or a software concept?
Software
Is a file a hardware or a software concept?
Software
Describe the main difference between a console and a GUI application.
A console application uses a simple text user interface. A GUI application uses graphics, menus, icons, etc.
Name several skills needed for software development.
Creating software architectures, understanding algorithms, fluency with programming languages, debugging, designing user interfaces.

## Slide 28: Review (cont’d):
What is the 8-bit binary representation for 6?
In Java, how many bytes are used to represent an integer (type int)?
Name several applications that run on the Internet.
What does TCP/IP stand for?
What is a search engine?
Notes: What is the 8-bit binary representation for 6?
00000110
In Java, how many bytes are used to represent an integer (type int)?
Four.
Name three applications that run on the Internet.
The World Wide Web, e-mail, AIM.
What does TCP/IP stand for?
Transmission Control Protocol / Internet Protocol
What is a search engine?
A program that helps to find documents on the Internet containing specified keywords or phrases.